IMPORTANT INFORMATION FOR VEHICLES FITTED WITH CHECK CONTROL MODULE (CCM)

NB:  Installation of this product requires connections to be made to the vehicle’s electrical system.  If you are in any doubt as to your ability to perform the installation, you must consult a qualified auto electrician to perform the installation for you.  When undertaking any work on a vehicle’s electrical system, we advise you to have a suitable, full-charged fire extinguisher rated for electrical fires readily to hand.

Neither the importer nor supplying dealer will accept any responsibility for any damage or loss, whether direct or consequential, arising from the installation of this product.

# If your vehicle is fitted with CCM, you can carry out the following simple modification to ensure both running lights on each side function as on the original lights.  Failure to do so will mean that only one running light will function on each side.  This is perfectly legal, so the modification is optional and is only for aesthetic purposes.

# Please refer to the diagram below:

NB: Disconnect the vehicle battery before attempting to make any modifications to the vehicle wiring, and when re-connecting the battery thereafter, verify that all electrical equipment fitted to the vehicle functions correctly before using the vehicle.

The pins on the wiring harness connector on the taillight unit are numbered as follows, looking at the lamp from the mounting side:

5 (  ( 1

6 (  ( 2

7 (  ( 3

8 (  ( 4

On the back of both lamp units, the metal tracks leading to pins four & eight must be bridged together using a piece of insulated automotive grade wire soldered to each track .

IMPORTANT: Ensure that any joints are properly insulated to prevent short circuits or fire risk.

DISCLAIMER:  WHILE THE ABOVE INFORMATION IS BELIEVED TO BE CORRECT & IS GIVEN IN GOOD FAITH, NEITHER ABCDESIGN NOR THE SUPPLYING DEALER WILL ASSUME ANY RESPONSIBILITY FOR LOSS OR DAMAGE, BE IT DIRECT, CONSEQUENTIAL OR OTHERWISE, WHICH IS INCURRED AS A RESULT OF ATTEMPTING THIS CONVERSION.

Ref. E36CoupeCCM